| GNL-5033xx (Φ5mm Flat Top TYPE) Ultra Brightness ABSOLUTE MAXIMUM RATING:(Ta=25℃) Parameter Unit DC Forward Current 30 mA Reverse Voltage 5 V Reverse Current (Vr-5V) 10 µA Peak Forward Current ,tw ,=1 msec Duty ,=1/20 150 mA Operation Temperature -40 +80 ℃ Storage Temperature -40 +100 ℃ Solder Dip (5 seconds,1.6mm from body ) Temperature 300 ±5 ℃ |  |
| --- | --- |
| Feature: 1.Small flange without stand-off 2.Long life-solid state reliability 3.Long lead length(25.4mm) 4.Versatile mounting on P.C. board or panel Description: 1.The shape of this series is round 2.General application is for indication,illumination,etc. 3.These LED lamps are available with a choice of defferent colors,light intensities,epoxy colors,etc. |
| Part Number EMITTED COLOR Lens Color Peak Wavelength (nm) Vf (v) Typ. IV (If=20mA) mcd View Angle 2θ1/2 Min. Typ. GNL-5033URC GaAlAs Super Red Water Clear 660 1.9 110 120 90° GNL-5033UEC AlGaInP Super Orange Water Clear 625 2.0 120 130 90° GNL-5033HRC AlGaInP Super Orange Water Clear 640 2.0 60 90 90° GNL-5033UGC AlGaInP Yellow Green Water Clear 572 2.0 50 70 90° GNL-5033UYC AlGaInP Super Yellow Water Clear 588 2.0 120 130 90° GNL-5033UBC InGaN Ultra Super Blue Water Clear 470 3.5 200 250 90° GNL-5033PGC InGaN Super Pure Green Water Clear 525 3.5 550 600 90° GNL-5033UEC-TL AlGaInP Super Orange Water Clear 625 2.0 300 320 90° GNL-5033UYC-TL AlGaInP Super Yellow Water Clear 588 2.0 300 320 90° GNL-5033UWC InGaN Super white Water clear 5500K-7000K 3.5 300 500 90° |

# Text boxes

G-NOR ELECTRONICS CO.,LTD.