| GNL-5053xx (Φ5mm ROUND TYPE) Ultra Brightness ABSOLUTE MAXIMUM RATING:(Ta=25℃) Parameter Unit DC Forward Current 30 mA Reverse Voltage 5 V Reverse Current (Vr-5V) 10 µA Peak Forward Current ,tw ,=1 msec Duty ,=1/20 150 mA Operation Temperature -40 +80 ℃ Storage Temperature -40 +100 ℃ Solder Dip (5 seconds,1.6mm from body ) Temperature 300 ±5 ℃ |  |
| --- | --- |
| Feature: Description: 1.Small flange without stand-off 1.The shape of this series is round 2.Long life-solid state reliability 2.General application is for indication,illumination,etc. 3.Long lead length(25.4mm) 3.These LED lamps are available with a choice of defferent 4.Versatile mounting on P.C. board or panel colors,light intensities,epoxy colors,etc. |
| Part Number EMITTED COLOR Lens Color Peak Wavelength (nm) Vf (v) Typ. IV (If=20mA) mcd View Angle 2θ1/2 Min. Typ. GNL-5053URC GaAlAs Super Red Water Clear 660 1.9 100 150 60° GNL-5053UEC AlGaInP Super Red Water Clear 625 2.0 100 200 60° GNL-5053HRC AlGaInP Super Red Water Clear 640 2.0 80 100 60° GNL-5053UYC AlGaInP Super Yellow Water Clear 590 2.0 80 130 60° GNL-5053UBC InGaN Super Blue Water Clear 470 3.5 300 400 60° GNL-5053PGC InGaN Pure Green Water Clear 525 3.5 400 500 60° GNL-5053BGC InGaN Super Cyan Water Clear 505 3.5 400 500 60° GNL-5053UGC AlGaInP Yellow Green Water Clear 572 2.0 100 200 60° GNL-5053UEC-TL AlGaInP Ultra Super Red Water Clear 625 2.0 300 400 60° GNL-5053UYC-TL AlGaInP Ultra Super Yellow Water Clear 590 2.0 300 400 60° GNL-5053UBC-TL InGaN Ultra Super Blue Water Clear 470 3.5 250 350 60° GNL-5053PGC-TL InGaN Ultra Super Green Water Clear 525 3.5 1000 1300 60° GNL-5053UWC InGaN Ultra Super White Water Clear 5500K-7000K 3.5 800 1200 100° GNL-5053UWC-Y InGaN Ultra Warm White Water Clear 2700K-3500K 3.5 800 1200 100° GNL-5053UWC-TL InGaN Ultra Super White Water Clear 5500K-7000K 3.5 1500 2000 100° |

# Text boxes

G-NOR ELECTRONICS CO.,LTD.