G-NOR ELECTRONICS CO.,LTD.

| GNL-20003xx (Φ20mm ROUND TYPE) Ultra Brightness ABSOLUTE MAXIMUM RATING:(Ta=25℃) | 3 4 1 2 |
| --- | --- |
| Parameter |  |  | Unit |  |
| DC Forward Current | 30 |  | mA |  |
| Reverse Voltage | 5 |  | V |  |
| Reverse Current (Vr-5V) | 10 |  | µA |  |
| Peak Forward Current ,tw ,=1 msec Duty ,=1/20 | 150 |  | mA |  |
| Operation Temperature | -40 | +80 | ℃ |  |
| Storage Temperature | -40 | +100 | ℃ |  |
| Solder Dip (5 seconds,1.6mm from body ) Temperature | 260 | ±5 | ℃ |  |
| Feature: 1.Small flange without stand-off 2.Long life-solid state reliability 3.Versatile mounting on P.C. board or panel Description: The shape of this series is round General application is for indication,illumination,etc. 3.These LED lamps are available with a choice of defferent colors,light intensities,epoxy colors,etc. |
| Part Number | EMITTED COLOR | Lens Color | Peak Wavelength (nm) | Vf (v) Typ. | IV (If=20mA) mcd | View Angle 2θ1/2 |
|  |  |  |  |  | Min. | Typ. |  |
| GNL-20003SRD | GaAlAs | Super Red | Red Diffused | 660 | 1.9 | 75 | 150 | 120° |
| GNL-20003LRD | GaAlAs | Super Red | Red Diffused | 660 | 1.9 | 100 | 200 | 120° |
| GNL-20003UED | AlGaInP | Super Orange Red | Red Diffused | 625 | 2.0 | 200 | 400 | 120° |
| GNL-20003UGD | AlGaInP | Yellow Green | Green Diffused | 572 | 2.0 | 150 | 300 | 120° |
| GNL-20003UYD | AlGaInP | Super Yellow | Yellow Diffused | 588 | 2.0 | 200 | 400 | 120° |
| GNL-20003UBD | InGaN | Super Blue | Blue Diffused | 470 | 3.5 | 250 | 400 | 120° |
| GNL-20003PGD | InGaN | Super Pure Green | Green Diffused | 525 | 3.5 | 900 | 1200 | 120° |
| GNL-20003WW | InGaN | Super White | White Diffused |  | 3.5 | 1000 | 2000 | 120° |
| GNL-20003UWW | InGaN | Super White | White Diffused |  | 3.5 | 1800 | 3500 | 120° |
| GNL-20003SRT | GaAlAs | Super Red | Red Clear | 660 | 1.9 | 90 | 180 | 60° |
| GNL-20003LRT | GaAlAs | Super Red | Red Clear | 660 | 1.9 | 120 | 240 | 60° |
| GNL-20003UET | AlGaInP | Super Orange Red | Red Clear | 625 | 2.0 | 240 | 480 | 60° |
| GNL-20003UGT | AlGaInP | Yellow Green | Green Clear | 572 | 2.0 | 180 | 360 | 60° |
| GNL-20003UYT | AlGaInP | Super Yellow | Yellow Clear | 588 | 2.0 | 240 | 480 | 60° |
| GNL-20003UBT | InGaN | Super Blue | Blue Clear | 470 | 3.5 | 300 | 480 | 60° |
| GNL-20003PGT | InGaN | Super Pure Green | Green Clear | 525 | 3.5 | 1200 | 2000 | 60° |
| GNL-20003WC | InGaN | Super White | Water clear |  | 3.5 | 2000 | 4000 | 60° |
| GNL-20003UWC | InGaN | Super White | Water Clear |  | 3.5 | 3000 | 5000 | 60° |